## Slide 1
Dian Lu (Ludian)
ASIPP, China
Dian.lu1997@gmail.com
12/12/2023
AI/ML for Fusion Challenge: Multi-Machine Disruption Prediction

## Slide 2
  The disruptive signals “LOOKS” different in the temporal domain.
  Train small models with small training datasets.
  It’s difficult to find the common features among the 3 devices:
  - System configurations are vastly different.
  - Positions of the coils and X-ray sightlines not given for the test set.
  - Time scale not specific for the test set.
2
Hypotheses Development
I

## Slide 3
2
Hypotheses Development
I
Normal
Disruptive
<- J-TEXT
C-Mod ->

## Slide 4
3
Methodology: Strategy
II
  Process each of the signal channels with small-scale CNNs (ssCNN), and connect them with a voting network.
  Signals chosen:
    Plasma Current (ip)
    Horizontal and Vertical Displacements (dx & dy)
    Plasma Density (ne)
    C3 Radiation (c3)
    Loop Voltage (vl)
    N = 1 Norm (n1n)
    Q95 (q95)
    IP Error (ipe)

## Slide 5
4
Methodology: Model Architecture
III
Final Rate
Channel Rate 1
Channel Rate 2
Channel Rate 3
Channel Rate 4
Channel Rate 5
Voting Network
ssCNN 1
ssCNN 2
ssCNN 3
ssCNN 4
ssCNN 5
Signal 1
Signal 2
Signal 3
Signal 4
Signal 5

## Slide 6
4
Methodology: Model Architecture
III

## Slide 7
3
Methodology: Model Architecture
III
  Adam Optimizer
  BCELoss Loss Function
  Multistep Learning Rate Scheduler
  Interpolate to normalize the signal lengths.
  Chop off ~ 60 ms at the end of the training signals.

## Slide 8
3
Methodology: Model Architecture
III
  Abnormally short signals (A very important criterion):
  - If the signal is shorter than a certain value, it is directly classified as disruptive.
  - Zero-padding the abnormally short signals.

## Slide 9
5
Results: Part 1
IV
  With only a single channel, the F1 score is about 0.73-0.79 (depending on which channel I choose).
  With the channels connected by the voting network, the F1 score is about 0.88-0.91 (depending on how I set the threshold).
  With the abnormally short signal criterion applied, the F1 score can reach 0.917.
  TP rate = 0.934, FP rate = 0.051

## Slide 10
6
Results: Part 2
IV
  ROC curve: